## Slide 1: Accelerated Geomorphic Response to Massive Sediment Loading by the 2008–2009 Eruption of Chaitén Volcano, Chile, Followed by Rapid Recovery
T.C. Pierson, J. J. Major
U.S. Geological Survey
Á. Amigo, D. Bertin
Servicio Nacional de Geología y Minería
A. Iroumé, H. Ulloa
Universidad Austral de Chile
A. Andreoli
Universidad de Concepción
J. Castro
Johannes Gutenberg Universität
SERNAGEOMIN, 23 May 2008

## Slide 2
Underlying Questions:
Explosive eruptions disturb fluvial systems. . . .
How do systems respond?
How do systems recover?
Fluvial system: Chaitén River Disturbance: 2008-2009 eruption of Chaitén Volcano, southern Chile

## Slide 3
Chaitén town
International Space Station, 2003
Old lava dome in caldera
STUDY AREA LOCATION
Northern Patagonia, Chile
43°S, 73°W
ASTER, 2 May 2008

## Slide 4
THE DISTURBANCE–
An initial explosive phase
First major high-silica rhyolite eruption (VEI 4-5) since Katmai, 1912
Starts late on 1 May 2008—27 hr after EQs first felt
Initial eruption puts ash column to ~18 km, lasts 6 hours
Nearly continuous ash emission with intermittent large explosions continued 2-8 May; ~ 1 km³ ejected; after 6 May ash is very fine
Explosive phase
Dome-building phase
UPI photo/Landov
Lava dome extrusion first detected 9 May 2008
Extrusion rates 20-100 m³/s
Volume ~0.5 km³ by Sep 08
Two dome-collapse pyroclastic flows enter Chaitén valley; 2nd is 3 – 5 M m³
Followed by a dome-building phase
SERNAGEOMIN

## Slide 5
Disturbance effects: (1) vegetation damaged/destroyed, and (2) hillslopes paved with nearly impermeable fine ash layers SURFACE RUNOFF increases
AND . . .

## Slide 6
Inputs of erodible tephra and volcaniclastic mass-flow deposits
Heavy sediment loading of rivers
Tephra on hillslopes: 3 to 100+ cm on 77 km² basin
Lithic pyroclastic flow deposits: up to 8 m thick, 2+ km long
PF deposits: Gravelly muddy sand textures. Dense glassy rhyolite with minor accidental granodiorite and greenschist (bedrock); trace of pumice.
Tephra: Coarse to extremely fine (silt-size) ash. Moderate- to low-vesicularity pumice (1.3-1.6 g/cm³), grading up to dense glassy rhyolite (2.1-2.5 g/cm³); trace of accidental lithics.

## Slide 7
Scale/sequence of erosion in Chaitén River

## Slide 8
Scale of eroded sediment volumes involved . . .

## Slide 9
Channel Aggradation 10 km Downstream of Volcano:
~4.5 m aggradation in first 24 hours
~7 m in first 48 hours
RF pulse 1 ≤ 3 mm/h
RF pulse 1 ≈ 20 mm
THE RESPONSE–
Initial sediment mobilization by modest rainfall

## Slide 10
Resulting flow in Chaitén River: A complex multi-day flood event
An initial lahar
Subsequent streamflow flood surges
4.5 m of aggradation in 24 hr; 7 m in 48 hr
Channel avulsion
Two deltas built
KEY
Lahar (~10⁶ m³) at base of section (yellow), hyperconcentrated flow-debris flow boundary
Highly concentrated transitional flow; upper flow regime (gray)
Muddy streamflow, shallow; upper flow regime (blue)

## Slide 11
Similar responses in other proximal fluvial systems:
Aggradation
Channel widening
Fining of channel beds
Braided channel patterns
Rayas River

## Slide 12
Estimated annualized sediment yield, based on delta growth rate over about 2 weeks is EXTREME.
(assume bedload = 20% of total load)

## Slide 13
IMPACTS IN CHAITÉN TOWN
Channel avulsion
1 – 3 m fluvial deposition

## Slide 14
IMPACTS IN CHAITÉN TOWN
Burial of much of town in sediment 1 - 3 m thick
Formation of new delta– extended 850 m from shore by 5 Dec 2008
Knickpoint retreat; streets become channels

## Slide 15
RECOVERY TRAJECTORY OVER 5 YEARS --
Distance across channel, in meters
Return to pre-eruption channel bed elevations within 4 - 5 years

## Slide 16
2008
2009
2010
2011
2012
RECOVERY TRAJECTORY OVER 5 YEARS --
Drastic decrease in sediment yield

## Slide 17
RECOVERY TRAJECTORY OVER 5 YEARS --
2009
2012
Black lines = pre-eruption active channel (2005)
Blue fill = active channel in the year indicated
Return to narrow, single-thread channel pattern

## Slide 18
RECOVERY TRAJECTORY OVER 5 YEARS --
Return to armored channel bed
May 2008
Jan 2011
Jan 2010

## Slide 19
TAKE-HOME MESSAGES (AND A QUESTION)
Severe downstream sedimentation triggered by relatively minor rainfall (est. 15-30 mm/24 hours; peak intensity <5 mm/h)
Downstream channel aggradation was extremely rapid following start of rainfall ( ~4.5 m in less than 24 hours; ~7 m in 48 hours)
Sediment mobilized (primarily from tephra mantle) by an initial lahar, followed by a complex multi-peaked flood involving pulses of hyperconcentrated flow and muddy streamflow
Peak annualized sediment yield from tephra flushing perhaps highest ever measured.
Erosion of valley-filling pyroclastic-flow deposits contributed to sustained high sediment yield (but much less than from tephra erosion).
Has this fluvial system truly recovered (stabilized)?