## Slide 1: The potential influence of the invasive plant, Impatiens glandulifera, on the hydro-geomorphic stability of inland river systems
P. Greenwood, W. Fister & NJ. Kuhn
Dept. Env. Sci., University of Basel, Switzerland
philip.greenwood@unibas.ch
Geological Society of America (GSA) Conference 2014, Vancouver, Canada

## Slide 2
I. glandulifera – Background info.
Common English name: ‘Himalayan Balsam’
Introduced UK & mainland Europe ca. 1850s
Highly invasive
Annual Plant – seasonal die-off
Notoriety – linked to soil erosion
Habitat preference: shady, damp, nutrient-rich soils – frequently disturbed…
…Riverbanks & Riparian Zone

## Slide 3
Distribution
Adapted from M. Winter, in Hejda, 2006
All temperate European countries
23/28 (i.e. ~ 82%) European Union (EU) states
Occupies > 50% rivers Czech Rep.
Occupies ~13% rivers UK
  est. £300 million to eradicate (US $447 million)
  Common parts east & west N. America
  New Zealand
  Globally prevalent

## Slide 4
Key Physiological Traits
No natural predators
Highly competitive
  over pollinate
  over produce nectar
  > 2,500 seeds per plant
  effective seed ejection mechanism (> 4 m)
Watercourses: transport seeds
Progressive downstream colonisation
Discrete ‘stands’
High density (> 40-50 m-2)
Reduced sunlight
Suppressed plant growth

## Slide 5
Key Lifecycle Traits
…underlying soil – susceptible to erosion?
Cold intolerant
Rapid die-back
Depleted / reduced vegetation cover…
July 2013
Dec 2013

## Slide 6
Hypothesis
…soil loss ‘contaminated’ sites > soil loss from [topographically] comparable areas supporting ‘natural’ vegetation…
PROVEN
Greenwood, P. & Kuhn, NJ. 2014. ‘’Does the invasive plant, Impatiens glandulifera, promote soil erosion along the riparian zone? An investigation on a small watercourse in northwest Switzerland’’. Journal Soils & Sediments 14(3): pp. 637-650.

## Slide 7
Results – R. Ibach 2012/13
Cont. Site ID | Estimated Area Cont. (m2) | Av. Net Δ Soil Profile (mm) | Total Equivalent Soil Loss (t ha.-1 yr.-1)
Site 1 | 8 | -15.84 | -261.6
Site 2 | 200 | -8.77 | -144.8
Site 3 | 6 | -5.12 | -84.5
Site 4 | 4 | -21.16 | -349.4
Site 5 | 3 | -77.84 | -1285.4
Site 6 | 150 | -11.61 | -191.8
Total | 371.00 | -140.34 | -2317.5
Whole stream length (ca. 10 km) extrapolated = I. glandulifera feasibly responsible mobilising additional ca. 100 t fine sediment!
Av. = 386 t ha.-1 yr.-1
Comparable - regions where high magnitude events regularly recorded

## Slide 8
Severe Erosion
Chart: Average Net Change Soil Surface (cm)
Contaminated | -1.164 | -1.59 | -0.87 | -0.51 | -2.11 | -7.78 | -1.04 | -0.82 | -0.41 | -0.3 | -1.91 | -7.536 | -3.09 | 0.92 | -0.32 | -1.48 | -2.35 | 0.25 | 1.75 | -17.23
Reference | -0.51 | -0.71 | 0.42 | -0.12 | 0.67 | -0.56 | 0.14 | -0.21 | -0.49 | -0.76 | 0.36 | -0.14 | 1.84 | 0.29 | 1.53 | 1.53 | 3 | -1.39 | -1.39 | 1.91
R. Ibach 2012/13 (206 d)
R. Ibach 2013/14 (176 d)
R. Taw 2013/14 (150 d)
Av. net erosion ≥ -2 cm = 6 sites (30%)

## Slide 9
Extreme Erosion
Chart: Average Net Change Soil Surface (cm)
Contaminated | -1.164 | -1.59 | -0.87 | -0.51 | -2.11 | -7.78 | -1.04 | -0.82 | -0.41 | -0.3 | -1.91 | -7.536 | -3.09 | 0.92 | -0.32 | -1.48 | -2.35 | 0.25 | 1.75 | -17.23
Reference | -0.51 | -0.71 | 0.42 | -0.12 | 0.67 | -0.56 | 0.14 | -0.21 | -0.49 | -0.76 | 0.36 | -0.14 | 1.84 | 0.29 | 1.53 | 1.53 | 3 | -1.39 | -1.39 | 1.91
R. Ibach 2012/13 (206 d)
R. Ibach 2013/14 (176 d)
R. Taw 2013/14 (150 d)
Av. net erosion ≥ -5 cm = 3 sites (15%)

## Slide 10
A Case of Extreme Erosion – R. Ibach 2012/13
Nov 2012
March 2013
Cause
I. glanduilfera colonisation
Dieback
Fine-substrate removal
Limited / no recolonisation (no viable seeds in seed-bank)
Effect
High magnitude erosion
Loss fine-substrate
Changes in riverbank morphology

## Slide 11
A Case of Extreme Erosion – R. Taw 2013/14

## Slide 12
Extreme Erosion? – R. Taw
Oct 2013
April 2014
CAUSE
I. glandulifera colonisation
Dieback
EFFECT
High magnitude scour erosion
[Formation] & Development valleys
Rapidly evolving morphology
No regrowth – Why?
Prime recolonisation territory
Repeat cycle?

## Slide 13
Growth/Maturity
Seed Ejection
Hydro-geomorphic instability?
Severe / Extreme Erosion
SPRING
SUMMER
AUTUMN
WINTER
Colonisation/Germination
Deposition/Invasion
Die-Off
Decomposition
Erosion
Depleted Veg.

## Slide 14
Hypothesis II
Continual cycles colonisation & dieback…
I. glandulifera – A ‘river system destabiliser’?
Induce hydro-geomorphic instability:
Moderate stream flow
Natural sustainable flood defence
Buffer fine-sediments & contaminants
Implications water quality
I. glandulifera: an erosion accelerant?
…often triggering severe / extreme erosion
Lack effective intervention measures = increasing encroachment

## Slide 15
Thank you for listening!