## Slide 1
GSA
20 YEARS OF CBM PRODUCTION AND MONITORING THE PINE RIVER SUBCROP.
NO DEPLETION
2014 October 19 • Vancouver, BC, CA
Presented by: Mr. Paul Oldaker
Graphic Arts by: Mr. Chris Chavez

## Slide 2
1971 USGS FASSETT AND HINDS, 2000 RMAG, OLDAKER
109°
36°
108°
107°
37°
Durango
Pagosa Springs
UT
Kkf
Kkf
Farmington
Pine River Gas Seep
CO
NM
AZ
50 Km
0
30 Mi
Cuba
Notes: Four Corners Area
San Juan Basin is third largest gas basin in the USA. Most of the formations produce oil, gas and/or water. Over 30 trillion CF produced so far from 1950..
Fruitland Formation is the most prolific coal bed methane formation in the world. Estimated 50 trillion CF originally in place.

## Slide 3
1889 CSM Lakes, 1924 Bayfield Blade, 1932 Durango Herald
1888
1924
1932-33
Notes: Long history of gas seepage from the Fruitland Formation.
1888- Animas Seep indentified
1924- Tendick Mine blowout like an out of control gas well.
1932 and 1933- Moving Mountain. A coal fire intersects a gas seep and causes explosions and landslides for 9 months.

## Slide 4
2011 October, Bayfield, Colorado, USA, Authors Collection
Notes: 1993- The Pine River began bubbling. Some accounts of this happening before.

## Slide 5
2010 October, Bayfield, Colorado, USA, Authors Collection
PINE RIVER ALLUVIUM
Kk
Kf
Kl
Kpc
Notes: Pine River alluvium- unconsolidated recently deposited sediments.
Lewis Shale (Kl)- marine mud with a transitional contact with…
Picture Cliffs Sandstone (Kpc)- marine beach sand with a distinct contact with…
Fruitland Formation (Kf)- fresh water swamps that formed thick and thin coal seams. A transitional contact with…
Kirtland Shale (Kk)- shale with thin coals.
All produce natural gas, oil and/or water in the SJB. Downhole video show gas in Kk,f,pc formations. CBM 50 trillion CF in Kf.

## Slide 6
2013 September 27 COGCC GIS System
PINE R. SEEPS
Notes: 50 Trillion CF gets a lot of interest.
About 2,000 Fruitland wells in the Colorado portion.

## Slide 7
2010 October, Bayfield, Colorado, USA, Authors Collection
Kk
Kf
Kl
Kpc
CBM NULL HYPOTHESIS
Notes: Led to the null hypothesis that the water pumping in the Fruitland for CBM caused water levels/pressures in the Fruitland were reduced and caused gas to be released at the subcrop.
Depends on the entire Fruitland being hydraulically connected.
Does not explain historical seepage.
Downward water flow and ascending gas flow at the same time is a problem.
Test by several methods.

## Slide 8
CBM, WATER, AND
SEEP PRODUCTION

## Slide 9
2014 April 26, Pine River Ranches Monitoring Report by Paul Oldaker
0.00
0.05
0.10
0.15
0.20
0.25
0
1,000,000
2,000,000
3,000,000
4,000,000
5,000,000
6,000,000
7,000,000
87
88
89
90
91
92
93
94
95
96
97
98
99
00
01
02
03
04
05
06
07
08
09
10
11
12
13
Pyramid Gas Flow, CFD
PRODUCTION CURVES AND GAS FLOW,
PINE RIVER RANCHES
Water 3 mile
Gas 3 mile
Pyramid Flow
P
R
R
S
E
E
P
S
E
P
9
3
9,244,858 bbl
29,719,208 bbl
1
3
O
F
3
W
E
L
L
S
8
7
2
O
F
5
W
E
L
L
S
8
8
2
O
F
7
W
E
L
L
S
8
9
1
2
O
F
1
9
W
E
L
L
S
9
0
5
O
F
2
4
W
E
L
L
S
0
4
O
F
2
8
W
E
L
L
S
0
4
4
O
F
3
2
W
E
L
L
S
0
5
1
O
F
3
3
W
E
L
L
S
0
6
Annual Gas Production in MCF
Annual Water Production in bbl
Notes: Within 3 miles of seeps 19 CBM wells were drilled and produced.
14 infill wells were then drilled.
Water production increases after new wells produced.
Gas production increases after new wells produced.
Seep production began 3 years after the first 19 wells were drilled. Then dropped before, during and after the infill wells were drilled. The seep production is acting differently than the CBM reservoir.
9 million bbl to start the seeps, but almost 30 million bbl produced to date.

## Slide 10
DOWNHOLE VIDEOS,
VERTICAL PRESSURES
BY PACKER TESTING

## Slide 11
1995 November, Bayfield, Colorado, USA, Authors Collection
Notes: 5 coals in the Fruitland nearest the seeps.
2 thin coals in the transition zone with the Kirtland.
Downhole video showed no gas in the lowest 4 coal seams. This is a real problem for the null hypothesis.
Desorbing gas in uppermost Fruitland coal seam. Location matches a secondary seep.
Six conventional gas zones in siltstones and sandstones in the Fruitland and transition zone. One matches primary seep. Another problem for the null hypothesis.
All were packer tested for pressures.

## Slide 12
2014 April 26, Pine River Ranches Monitoring Report by Paul Oldaker
-300
-280
-260
-240
-220
-200
-180
80
90
100
110
120
130
140
150
Depth, ft
Pressure, psig
SALMON 2 PACKER TESTS, PINE RIVER RANCHES
Test Zone
Hydrostatic
OVERPRESSURE
UNDERPRESSURE
Test 1=149 psi
Test 2=122 psi
Test 3=108 psi
Test 4=113 psi
Test 5=118 psi
Test 6=122 psi
Test 7=128 psi
-
-
-
288 ft=Top of Fruitland
215 ft=
Video of
Siltstone Gas
299 ft=Video of Displacement Gas
Notes: Define normal, over and under pressure.
Video show gas in transition zone which matches a large overpressure area.
No under pressure due to CBM production. Bad for the null hypothesis.

## Slide 13
TEMPERATURE TRACER,
GEOTHERMAL GRADIENT

## Slide 14
2014 April 26, Pine River Ranches Monitoring Report by Paul Oldaker
-110
-90
-70
-50
-30
-10
8
9
10
11
12
13
14
Depth, ft
Transducer Temperature, C
GEOTHERMAL GRADIENT, PINE RIVER RANCHES
Qal, James 2, 17 Year Mean
Fruitland Bedrock, 20 Year Mean
Geothermal Line
Qal, Pick Bar, 20 Year Mean
WATER
COLD PINE RIVER
ALLUVIAL
FLOWING DOWN INTO
WARMER BEDROCK
WATER
COLD PINE RIVER
ALLUVIAL
FLOWING DOWN INTO
WARMER BEDROCK
Notes: Normal geothermal gradient outside the seep.
If colder water at depth then alluvial water is going down into the Fruitland.
If hotter water at surface then warmer Fruitland water is going up into the alluvium.
The winner is warmer water going up. Strong measurements that the stream is not being depleted. Bad for the null hypothesis.

## Slide 15
CATION WATER QUALITY

## Slide 16
2014 April 26, Pine River Ranches Monitoring Report by Paul Oldaker
0
10
20
30
40
50
60
70
80
90
100
Sodium %
2000 SODIUM % COMPARISON, PINE RIVER RANCHES
Notes: Bedrock wells are high in sodium.
Alluvium and river are low in sodium.
No bedrock wells with low sodium. No flow from alluvium to bedrock.
One alluvial well with high sodium. Flow was from bedrock to alluvium.

## Slide 17
WATER AGE

## Slide 18
2003 Snyder et al. Figure 16
Notes: Snyder et al. 2003 (Rice University) used iodine 129 to age very old Fruitland waters.

## Slide 19
2003 Sanford and Sorek
Notes: Sandford and Sorek (CSU) used helium 4 to age very old Fruitland waters,

## Slide 20
Data from Snyder et al 2003
Notes: Snyder et al. also took chlorine 36 a true radioisotop. The youngest water was a well about 1.5 mile from the Pine River seeps. The result was half million year old water. Indicates a very closed system.

## Slide 21
AREAL POTENTIOMETRIC
HEAD TRENDS

## Slide 22
1955-1994, Bayfield, Colorado, USA, Authors Collection
Notes: Pre development potentiometric surface.
CBM wells.
Downbasin monitor wells.
Subcrop monitor wells.
All should decline if all connected.

## Slide 23
2014 April 26, Pine River Ranches Monitoring Report by Paul Oldaker
FRUITLAND POTENTIOMETRIC HEAD
PINE RIVER RANCHES
1 OF 33 WELLS 2006
4 OF 32 WELLS 2005
5 OF 24 WELLS 2001
4 OF 28 WELLS 2004
Potentiometric Head, ft amsl
7,190
7,170
7,150
7,130
7,110
7,090
7,070
7,050
7,030
7,010
6,990
6,970
6,950
6,930
1994
1995
1996
1997
1998
1999
2000
2001
2002
2003
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
+
+
GURR
GURR
POLE BARN
KILLIAN DEEP
JAMES 1
KILLIAN SHALLOW
SALMON 3
SALMON 3
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Notes: Nearest downbasin monitor wells declined, but 2-3 years after seep.
Subcrop monitor wells did not decline and show seasonality.
Neither sets of monitor wells reacted to the infill wells.
There is a hydraulic boundary between the CBM production and the suncrop.

## Slide 24
2014 April 26, Pine River Ranches Monitoring Report
DOES NOT EXPLAIN HISTORICAL SEEPAGE,
SEEP PRODUCTION DIFFERENT THAN CBM,
SEEP PRODUCTION DOES NOT REACT TO INFILL
VIDEO- SEEP DIFFERENT ZONES THAN CBM,
OVERPRESSURED NOT UNDERPRESSURED,
TEMPERATURE- FLOW FROM BEDROCK TO Qal,
WATER WAS TOO OLD BY AGE ISOTOPES,
BOUNDARY BETWEEN CBM AND SUBCROP,
I REJECT THE NULL CBM HYPOTHESIS,
NO DEPLETION.
CBM NULL HYPOTHESIS

## Slide 25
2014 April 26, PRR Report and USBOR Vallecito Precipitation Record
0.06
0.11
0.16
0.21
0.0
1.0
2.0
3.0
4.0
5.0
6.0
7.0
8.0
9.0
1999-Jan-01
1999-Apr-02
1999-Jul-02
1999-Oct-01
1999-Dec-31
Pyramid Gas Flow, CFD
Precipitation, in
1999 PRECIPITATION AND PYRAMID GAS FLOW,
PINE RIVER RANCHES
PRECIPITATION
MONTHLY PRECIPITATION
GAS FLOW
17.71 in HIGHEST
JUL, AUG, SEP PRECIPITATION
IN 71 YEAR
RECORD
H
I
G
H
R
I
V
E
R
I
N
U
N
D
A
T
E
S
M
E
T
E
R
Notes: 1999- July, August, September precipitation was over 17 inches.
With continued precipitation the gas flow rate went up.
When precipitation ended in October, November and December the gas flow rate went down.
March gas flow peak was due to low altitude snowmelt.
Also a new seep, the Tertiary seep trend was identified.

## Slide 26
2014 April 26, PRR Report and USBOR Vallecito Precipitation Record
0.06
0.11
0.16
0.21
0.0
1.0
2.0
3.0
4.0
5.0
6.0
7.0
8.0
9.0
2002-Jan-01
2002-Apr-02
2002-Jul-02
2002-Oct-01
2002-Dec-31
Pyramid Gas Flow, CFD
Precipitation, in
2002 PRECIPITATION AND PYRAMID GAS FLOW,
PINE RIVER RANCHES
PRECIPITATION
MONTHLY PRECIPITATION
GAS FLOW
17.23
in THIRD
LOWEST ANNUAL PRECIPITATION IN 71 YEAR RECORD
Notes: 2002- Same scale as previous graph. Just over 17 inches of precipitation in entire year. A real drought.
Gas flow rate for entire year was much reduced.
Again July, August and September had rain and gas flow rate increased with it.
Another February gas flow peak due to low altitude snowmelt.

## Slide 27
Kk
Kl
Kpc
KkKf
2010 October, Bayfield, Colorado, USA, Authors Collection
PRECIPITATION HYPOTHESIS- 2000
Kf
Notes: In 2000 I formed the precipitation null hypothesis.
An overpressured Transition zone.
As rain continues, water levels in the transition zone rise and push out more gas.

## Slide 28
TEST BY SEEP PRODUCTION
AND CUMULATIVE
EXCESS, DEFICIT ANALYSIS

## Slide 29
2014 April 26, PRR Report, 1999 CWRRI, Drought in Colorado, NOAA
-0.18
-0.15
-0.12
-0.09
-0.06
-0.03
0.00
0.03
0.06
0.09
0.12
0.15
0.18
-40
-35
-30
-25
-20
-15
-10
-5
0
5
10
15
20
25
30
35
40
1880
1890
1900
1910
1920
1930
1940
1950
1960
1970
1980
1990
2000
2010
Mean Annual Pyramid Gas Flow, CFD
Precipitation Accumulated
Excess/Deficit, inches
Year
PRECIPITATION ADJUSTED ACCUMULATED EXCESS/DEFICIT, PINE RIVER
RANCHES
DURANGO
VALLECITO
PYRAMID FLOW
R
1
8
8
8
C
A
R
B
O
N
J
U
N
C
T
I
O
N
S
E
E
P
1
9
2
4
T
E
N
D
I
C
K
M
I
N
E
G
A
S
S
E
1
9
3
2
M
O
V
I
N
G
M
O
U
N
T
A
I
N
1
9
9
1
V
A
L
E
N
C
I
A
C
A
N
Y
O
N
S
E
E
P
1
9
9
3
P
I
N
E
R
I
V
E
R
S
E
E
P
1
9
9
9
T
E
R
T
I
A
R
Y
S
E
E
P
Notes: Durango record is longest in area, about 20 miles from site. Vallecito record is closest to site at 6 miles north. Periods of excess and deficit.
Gas seep observations match excess periods. 1930’s, 1940’s, 1950’s, 1960’s, 1970’s have no seep observations even though SJB was crawling with uranium prospectors, Sandstone gas boom, coal mine boom and formation of the Four Corners Geological Society.
Gas Flow matches red Vallecito line.

## Slide 30
2014 April 26, PRR Report, 1999 CWRRI, Drought in Colorado, NOAA
0.00
0.03
0.06
0.09
0.12
0.15
0.18
0
5
10
15
20
25
30
35
40
1992
1993
1994
1995
1996
1997
1998
1999
2000
2001
2002
2003
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
Mean Annual Pyramid Gas Flow, CFD
Precipitation Accumulated Excess/Deficit, inches
Year
PRECIPITATION ADJUSTED ACCUMULATED EXCESS/DEFICIT
PINE RIVER RANCHES
VALLECITO
PYRAMID FLOW
S
E
C
O
N
D
A
R
Y
S
E
E
P
I
D
E
N
T
I
F
I
E
D
1
9
9
3
P
I
N
E
R
I
V
E
R
P
R
I
M
A
R
Y
&
N
1
9
9
9
T
E
R
T
I
A
R
Y
S
E
E
P
I
D
E
T
I
F
I
E
D
2
0
0
4
T
E
R
T
I
A
R
Y
S
E
E
P
C
E
A
S
E
S
2
0
0
5
T
O
2
0
0
7
V
E
G
I
N
V
A
S
I
O
N
2
0
0
9
T
O
2
0
1
2
I
N
T
E
R
M
I
T
E
N
T
S
E
E
P
S
V
E
G
I
N
V
A
S
I
O
N
Notes: Very similar lines.
Seep observations match.
1993 Primary and secondary seep trends identified.
1999 Tertiary seep trend identified.
2002 Drought year
2004 Tertiary seep ceases.
2005 Vegetation invasion began.
2009 Primary and Secondary seeps go intermittent.

## Slide 31
2014 April 26, PRR Report and NOAA Vallecito Precipitation Record
Notes: Cross plot is direct relation.
About 10 inches of cumulated excess needed to start.
Gas flow rate caps, probably due to low permeability.

## Slide 32
2014 April 26, Pine River Ranches Monitoring Report
CUMULATIVE EXCESS PRECIPITATION
EXPLAINS EPISODIC HISTORICAL SEEPS,
CUMULATIVE EXCESS PRECIPITATION
DIRECTLY RELATED TO CURRENT SEEP
PRODUCTION,
I CONTINUE TO ACCEPT THE NULL PRECIPITATION HYPOTHESIS AFTER 13 YEARS AND COUNTING.
PRECIP. NULL HYPOTHESIS-OLDAKER 2000

## Slide 33
THANKS TO Bp and PETER FALK
PAUL OLDAKER
HYDROGEOLOGIST
P.O. BOX 27090
FEDERAL WAY, WA
98093
970-846-0082
pauloldaker@netscape.com